## Slide 1: ADA Threshold and Basic Design ADA 2.0
Kristie Billiar | ADA Policy Program Manager
November 8, 2017

## Slide 2: Thresholds (what to do when)

## Slide 3: Using Your Transition Plan
Your transition plan has identified what need to be done and the law defines when it needs to be done
The transition plan serves two functions it sets the baseline to measure progress and gives a broad outline for investment and scoping
Facilities are an asset and condition is related to their accessibility

## Slide 4: Alteration Threshold
Curb ramps must be done whenever there is alteration level work
The accessibility improvements must be done AT THE SAME TIME or PRIOR to the alterations work.
There are tradeoffs with either approach

## Slide 5: Right of Way and Alterations
Public entities are required to obtain Right of Way to provide accessibility when needed.
If right of way is not obtained and the facility is non compliant the entity must be able to demonstrate that reasonable efforts were made to obtain it

## Slide 6: Alteration Work Types
Mill and Overlay
Mill and fill
Addition of New Layer of Asphalt,
Hot In-Place Recycling,
Open-graded Surface Course,
Thin lift overlays
Micro-surfacing,
Cape Seals,
Asphalt and Concrete Rehabilitation,
Concrete repair: Isolated, partial and/or full-depth repairs to restore functionality of the slab; e.g., edge spalls, corner breaks Bridge joint replacement
Bridge Deck Overlays
The DOJ has identified the following work types as an alteration:

## Slide 7: Maintenance Work Types
Asphalt crack sealing
Bituminous pavement seal coat
Chip sealing
Isolated concrete dowel-bar retrofit
Concrete joint sealing
Concrete pavement surface planning / diamond grinding
Slurry seals
Bridge substructure preservation: concrete and steel
Bridge superstructure activities: Painting, bearing rehabilitation/replacement and barrier/guardrail/railing restoration.
Surface Sealing
Fog Seals
Scrub Sealing
Joint Crack Seals
Joint repairs
Spot High-Friction Treatments
The DOJ has identified the following work types as maintenance:

## Slide 8: Maintenance Work
Accessibility improvements are not required with maintenance activities
Doing two or more maintenance activities may trip the alterations threshold, but this is not well defined

## Slide 9: Accessible Design (what is it)

## Slide 10: The Basics
ADA is an element of good pedestrian design and complete street concepts
Design that is focused only on ADA is difficult to maintain and can unintentionally refocus the context of the corridor.
Rather than focus on compliance MnDOT advises focusing on usability, maintainability, and constructability
Slopes and dimensions are absolute; ADA/PROWAG allows no tolerances

## Slide 11: Pedestrian Access Route
Pedestrian Access Route (PAR)
  All the navigable elements that work together to allow pedestrians to move from place to place
  Sidewalk or trail, curb ramp, crosswalks, and APS
  PAR by definition is accessible to all pedestrians

## Slide 12: Zone System
Establishing a buffer area between sidewalk and traffic creates a safer and more pleasant place to walk and makes it easier to meet all ADA requirements

## Slide 13: Zone System: Residential

## Slide 14: Zone System: Commercial

## Slide 15: Zone System: Doorways
Maintain a 5-ft.-wide path when doors of a building are open
3 ft. clearance recommended between building and PAR when doors open toward the pedestrian way

## Slide 16: Sidewalk Basics
ADA is an element of good pedestrian design:
  Clear of obstructions
  4 ft. minimum width (5 ft. minimum MnDOT)
  Smooth paved surface
  2% maximum cross slope (1.5% Mn/DOT desired)
  Level and continuous across driveways

## Slide 17: Sidewalk Basics: Obstacles (NO!)
Randomly arranged street furnishings are hazardous clutter.

## Slide 18: Sidewalk Basics: Obstacles (NO!)
Utilities, poles and boxes pose obstacles.

## Slide 19: Sidewalk Basics: Obstacle Mitigation
Sidewalks or trails can wrap around obstacles.

## Slide 20: Sidewalk Basics: Cross Slope
Steep cross slopes are inconvenient and hazardous
Require extra effort by wheelchair users to move forward
Become slippery when wet, icy or snowy

## Slide 21: Sidewalk Basics: Driveways
Driveway crossings without level landings force users to travel over the sidewalk flare.
Results in abrupt changes in cross slope
Compromises balance and stability for wheelchair users and a hazard for many others

## Slide 22: Sidewalk Basics: Driveways
The easiest way to maintain level passage is with sidewalks separated from the road.

## Slide 23: Sidewalk Basics: Surface
Bricks, cobblestones and other textured pavement create:
Increased rolling resistance
Tripping hazards
Painful vibrations to people with brittle bones or spinal cord injuries in wheelchairs
Potential maintenance issues
Strongly discouraged by PROWAG

## Slide 24: Sidewalk Basics: Surface
Tolerances:
Up to 1/4 inch, no treatment
1/4 to 1/2 inch, bevel the surface, with maximum grade of 50%
More than 1/2 in, replace the sidewalk panel

## Slide 25: Sidewalk Basics: Continuity/network
Avoid sidewalks to nowhere

## Slide 26: Curb Ramp Basics
Minimum 4 ft. wide Pedestrian Access Route (PAR) with a maximum cross slope of 2%
Landing dimensions 4 ft. by 4 ft. minimum with a maximum 2% slope in all directions
If longitudinal slope exceeds 5%, landings must be provided on any pedestrian facility
Maximum ramp slope is 8.3%
Maximum length of ramp is 15 ft.

## Slide 27: Curb Ramps: Types
Perpendicular ramp
Parallel ramp
One-way directional ramp
Two-way directional ramp
Depressed corner
Fan ramp
Tiered ramps
Diagonal ramps (not recommended)

## Slide 28: Perpendicular Ramp
Ramp is perpendicular to the curb line.
Grade break occurs at the top of the ramp and the flow line

## Slide 29: Parallel Ramp
Parallel to the curb line
Used with narrow sidewalks and in tight ROW situations
Slope of curb should match slope of ramp

## Slide 30: One Way Directional
Grade break occurs at the front edge of the truncated domes and shall be perpendicular to the direction of travel.

## Slide 31: Two-Way Directional
Two ramps with a shared landing
If ramps are directional, the grade break should be at the front of the truncated domes.

## Slide 32: Depressed Corner
Radial truncated domes from outside edge of crosswalk to outside edge of crosswalk
Entire area at 2% maximum slope with parallel ramps/blended transitions rising from the depressed corner

## Slide 33: Fan
Ramp slope through the radial truncated dome area with a landing at the top of the ramp
Most difficult type of curb ramp to construct correctly

## Slide 34: Design Standards (what to do)

## Slide 35: ADA Minimums
Minimum design approach
  Meets minimum ADA Requirements
  Minimal use of Public Right of Way Guidance (Access Board)
  Rarely acquires ROW or uses innovative design
  More successful in residential areas versus commercial
  Does not always mitigate liability

## Slide 36: MnDOT Design Approach
PROWAG is the basis for MnDOT’s Design Standards
Mn/DOT sees PROWAG as a valuable tool in new construction and in improving quality of existing accommodations.
It helps ensure that the same degree of use and access provided to the general public is also available to pedestrians with disabilities.

## Slide 37: MnDOT Standards
MnDOT Requirements
  Curb Ramp Standard Plans
  Road Design Manual 11-3
  Special Provisions for Construction

## Slide 38: Exceptions
Improvements are not required if they would significantly expand project scope. Examples:
  Relocating utilities (more that a hand hole)
  Providing drainage work
  Scope and cost go hand in hand
The earlier the needed improvements are identified—preferably in the project scoping phase—the more likely they will fit within budget and schedule.

## Slide 39: Technically Infeasible
Technical feasibility
  Governed by limiting factors in the project area. These may be temporary (a drainage structure) or permanent (adjacent buildings or terrain)
  “Too expensive” is not a factor in technical infeasibility at a project level.
  Cost can be a factor if it poses a programmatic burden on a city, county or state

## Slide 40: Maximum Extent Feasible
Maximum extent feasible
  How close a project can come to full accessibility and adherence to standards, given site constraints
  Can be seen as the best solution, working within technical feasibility limitations
  Cost or funding does not determine the maximum extent feasible

## Slide 41: Scoping – Design - Result
A mill and overlay project would typically include upgrading curb ramps…
…unless a complicating factor, such as the catch basin shown below, made the improvement unfeasible within the scope of the original project

## Slide 42: Final Thoughts
Aim for GOOD DESIGN, which
meets standards to maximum extent feasible
fits the context
offers a usable solution
Good design does not mean simply applying a standard without considering context.
In certain circumstances, departing from a standard for a good reason may be better than following a standard to the letter.

## Slide 43: Thank you again!
Kristie Billiar
kristie.billiar@state.mn.us
651-366-3174