Work Type Definition

Pages 1-2 detail the work type definition.  In order to become pre-qualified for this work type, please see the “Work Type Submittal Requirements” on pages 3-4.

- Description

  - Video recording of inspection of stormwater system features (pipes, culverts, manholes, catch basins, drop inlets, aprons, etc) conducted using remote controlled, self-propelled, video cameras.

  - Any suspected illicit discharges to the drainage system shall be reported.

- Standards and Specifications

Standards and specifications required for a project under this work type may include the following:

  - Traffic Control - Traffic control and lane closures must be conducted in accordance with the Minnesota Manual of Uniform Traffic Control Devices and, in the Metro Area must be coordinated with Dispatch (651-582-1550).  Traffic Control is solely the responsibility of the consultant/contractor to arrange.

- Provided By MnDOT

Information to be supplied by MnDOT for a project may include the following:

A.  All information will be provided electronically:

- Project Plan Sheets

- Map of surveyed feature locations (fip files) or GIS Feature Class

- Map of existing HYDINFRA features (known stormwater system features)

- Id numbers of known features

- Provided by Consultant

Deliverables to be supplied by the consultant for a project may include the following:

  - Video:

- Video inspections shall be carried out at a slow rate of speed, sufficient to inspect defects of the stormwater system feature.

- Lighting shall be sufficient to illuminate the entire inner circumference of the feature from the camera to approximately 10-20 feet ahead of the camera.

- The video must be in color, indexed, and in digital format (MPEG-1 or MPEG-4).

- Video files must contain only one feature, i.e. one pipe run, one structure, etc.  Video files containing more than one feature per file will be considered non-satisfactory.

- Video inspection shall include providing video of the entire feature (completing a 360 degree pan of each broken, separated, or otherwise damaged joint and/or crack encountered in pipes, completing a top-to-bottom pan of the entire inner circumference of manholes/catch basins/drop inlets, etc)

- Defects along the pipe are to be identified, indexed, and stamped into the video on the screen to allow for easier processing by MnDOT personnel.

- Audio commentary regarding beginning point, ending point, approximate bearing, structure feature diameter/size, material, length, height, defects, and condition and rating is required.

- Any illicit discharges to the drainage system shall be reported.

  - Maps:

- Maps must be in ArcGIS, ArcMap, DXF, or MicroStation format.

- Electronic map and with flow arrows showing stormwater system features connectivity and flow directions.

- All map and map edits must be returned to the State.

- Map edit’s must be legible and need to distinguish all known features according to unique identification number system provided by State.

  - Illicit Discharge Reporting

- Suspected Illicit Discharges should immediately be reported to Dispatch at 651-582-1550 (Metro Area) or to the appropriate contact in the HYDINFRA Ratings Guide (Outside the Metro Area).

The balance of this page is intentionally left blank.

Work Type Submittal Requirements

A consultant firm becomes pre-qualified based on the qualifications of the personnel that are employed by the firm and by meeting the demonstrated requirements.

| Key Personnel Requirements |
| --- |
| Minimum Number of Staff: | Two HYDINFRA –trained video equipment operators/inspectors. |
| Professional Certification/Licensure: | Current HYDINFRA certification is required (MnDOT will provide training. MnDOT Contact for Training is Bonnie Peterson: 651-366-4470. Note that there is an Equipment requirement for training: Trimble ProXR or other GPS unit capable of using HYDINFRA data dictionaries is required for training in HYDINFRA by MnDOT Personnel) |
| Work Type Submittal Requirements* |
| Resume and Relevant Project Experience Form (Form PQ1) | Complete Parts, 1, 1A, and 2of form PQ1 Part 1: Fill out general information and names of personnel, including other professional and technical support personnel. Part 1A: Fill out for each person listed in Part 1. Experience of the qualified staff must be demonstrated by reference to completed stormwater system feature video recording and inspection projects* (minimum of three for each staff member up to five) within the last five years. Part 2: Project Examples listed must correlate to those described below in “ Project Example Requirements” Part 3: Not applicable for this work type |
| Project Example Requirements | Submit one previous project* in storm water system feature video recording and inspection, completed in the last 5 years. Project example must be: Files containing video images of stormwater feature interiors with problem areas identified and marked on video. Electronic map showing connections, unique ID number and flow directions between stormwater features. *For the purposes of the submittal, a “project” is defined as a segment or corridor defined by the owner/client such as MnDOT’s State Project (SP) numbers. There may be more than one “project” (multiple SPs) under an individual contract. |
| Proof of Professional Certification/ Licensure | Provide a copy of HYDINFRA certification |
| *Work Type Submittal Instructions: Create a flash drive that includes the following individual files or folders in this order: I. Resume and Relevant Project Experience Form (Form PQ1) II. Project Example Requirements (this should be a folder that includes individual files clearly named according to Part 2 of the PQ1) III. Proof of Professional Certification/Licensure Each file should be saved in the format identified above. Submit 5 copies of the flash drive. |