Work Type Definition

Page 1 details the work type definition.  In order to become pre-qualified for this work type, please see the “Work Type Submittal Requirements” on page 2.

- Description

This type of work requires testing various materials in accordance with the proper procedure, reporting results compared to the corresponding specifications, and making recommendations for materials disposition (if required).

- Standards and Specifications

Standards and specifications required for a project under this work type may include the following:

- Reporting must meet requirements of AASHTO R 18 and recommendations.

- Trained personnel with calibrated equipment will perform all test procedures in accordance with the requested standard.

- Electronic test data must be compatible with the current database structure of MnDOT.

- The laboratory, not the company, performing the testing must be accredited by the AASHTO Materials Reference Laboratory (AMRL) or a comparable laboratory accreditation program approved by MnDOT and the FHWA for all test procedures performed.  Use the website below to verify which laboratories are accredited in which tests, as the prequalification list is only for general approval. A list of the currently accredited laboratories and the tests in which they are accredited can be found at www.amrl.net/amrlsitefinity/default/aap/r18labs.aspx.

- Provided By MnDOT

Information to be supplied by MnDOT (if not available on MnDOT web site) for a project may include the following:

- MnDOT Manuals (Laboratory, Concrete, Grading and Base, Bituminous), MnDOT Standard Specifications for Construction, and Special Provisions of the Contract

- Provided by Consultant

Deliverables to be supplied by the consultant for a project may include the following:

- Final Materials Test Report meeting the requirements of AASHTO R 18 and recommendations

(if required).

- Final Materials Test Report (both paper and electronic) submitted to requestor upon completion and in conformance with the negotiated time requirements and frequency.

This remainder of this page is intentionally left blank.

Work Type Submittal Requirements

A consultant firm becomes pre-qualified based on the qualifications of the personnel that are employed by the firm.

| Key Personnel Requirements |
| --- |
| Minimum Number of Staff: | At least one professional civil engineer with relevant experience Sufficient production staff |
| Professional Certification/Licensure: | Qualified professional civil engineer must be a licensed Civil Engineer with the Minnesota State Board of Professional Engineers. All certifications and licenses required by AASHTO R 18, “Establishing and Implementing a Quality System for Construction Materials Testing Laboratories” and technical certifications required by MnDOT specifications for the testing performed. |
| Work Type Submittal Requirements* |
| Resume and Relevant Project Experience Form (Form PQ1) Submit in Word format | Complete Parts 1, 1A, 2 and 3 of Form PQ1 Part 1: Fill out general information and names of personnel Part 1A Qualifying experience of staff must be documented by personal experience histories of the firm's principals or key personnel. Personnel requirements of the qualified staff must be demonstrated by reference to completed qualifying requirements of AASHTO R 18. The laboratory, not the company, performing the testing must be accredited by the AASHTO Materials Reference Laboratory (AMRL) or a comparable laboratory accreditation program approved by MnDOT and the FHWA for all test procedures performed. Sufficient production staff must also be documented. *To be a part of this work type, firms do not have to be accredited laboratories in all fields. A list of the currently accredited laboratories can be found at http://www.amrl.net/amrlsitefinity/default/aap/r18labs.aspx. Please verify with this site that your laboratory is currently accredited prior to applying for prequalification for this work type with MnDOT. Part 2: Not applicable for this work type. Part 3: Document production staff of company. |
| Proof of Professional Certification/Licensure Submit in PDF format | Provide current copies of all required licenses and certifications for key personnel and the laboratory. |
| *Work Type Submittal Instructions: Create a flash drive that includes the following individual files or folders in this order: I. Resume and Relevant Project Experience Form (Form PQ1) II. Proof of Professional Certification/Licensure Each file should be saved in the format identified above. Submit 5 copies of the flash drive. |