Work Type Definition

Page 1 details the work type definition.  In order to become pre-qualified for this work type, please see the “Work Type Submittal Requirements” on page 2.

- Description

Investigations will identify and locate, both horizontally and vertically, significant soil and rock types, ground water conditions, and establish the characteristics of the subsurface materials visually, by sampling, and by laboratory and in-situ testing. The methodology involved includes on-site investigations by performing Standard Penetration tests and rock coring. Specialized test equipment may also be required, such as the field vane shear, pressure meter, or dilatometer. This work type also includes the installation of instrumentation such as piezometers and slope indicators.

- Standards and Specifications

Standards and specifications required for a project under this work type may include the following:

- All tasks will be performed in accordance with current ASTM, AASHTO, and MnDOT standards and specifications.  All investigations will be conducted in accordance with current Minnesota Department of Health Regulations. The current Specifications for Subsurface Investigation & Geotechnical Analysis and Design Recommendations can be found at http://www.mrr.dot.state.mn.us/geotechnical/foundations/tcontract/consultdrillreport.doc.

- Provided By MnDOT

Information to be supplied by MnDOT for a project may include the following:

- Plans showing existing topography, proposed alignments, and locations of the existing and proposed structures.

- Information (plans) showing property ownership information for boring locations off of State Right-of-Way.

- Bridge benchmark information for determining boring elevations.

- American Society for Testing and Materials (ASTM), American Association of State Highway & Transportation Officials (AASHTO), and MnDOT Standard Specifications.

- Provided by Consultant

Deliverables to be supplied by the consultant for a project may include the following:

- Final Standard Penetration Test (SPT) and/or Rock Coring Investigation Report

  - Final Boring Logs in hard copy and electronic format (.gpj)

  - A copy of the driller’s field boring logs and samples if required.

  - Weekly progress reports.

  - SPT hammer calibration reports.

  - Minnesota Department of Health sealing records.

This remainder of this page is intentionally left blank.

Work Type Submittal Requirements

A consultant firm becomes pre-qualified based on the qualifications of the personnel that are employed by the firm and by meeting the demonstrated requirements.

| Key Personnel Requirements |
| --- |
| Minimum Number of Staff: | At least one employee with the relevant qualifying experience and one employee with a Minnesota Department of Health License for Monitoring Well Contractor (or equivalent). One employee may be allowed if that person meets both of these requirements. |
| Professional Certification/Licensure: | Monitoring Well Contractor (or equivalent) |
| Work Type Submittal Requirements* |
| Resume and Relevant Project Experience Form (Form PQ1) Submit in Word format | Complete Parts 1, 1A, 2 and 3 of Form PQ1 Part 1: Fill out general information and names of personnel Part 1A: Qualified employee must have a minimum of 5 years experience in the activities required. Satisfactory experience must be demonstrated on at least two projects (maximum of five) in the last five years in the activities required. Part 2: Examples should correlate to “”Project Example Requirements” section. Part 3: Provide list of production staff sufficient to conduct testing. |
| Project Example Requirements Submit in PDF format | Submit one example for each proposed person. Example must be from a project completed within the last five years. Example must be a boring log. |
| Proof of Professional Certification/Licensure Submit in PDF format | Provide current copy of applicable Professional Certification/Licensure. |
| *Work Type Submittal Instructions: Create a flash drive that includes the following individual files or folders in this order: I. Resume and Relevant Project Experience Form (Form PQ1) II. Project Example Requirements (this should be a folder that includes individual files clearly named according to Part 2 of the PQ1) III. Proof of Professional Certification/Licensure Each file should be saved in the format identified above. Submit 5 copies of the flash drive. |