## Slide 1: 2018 Pavement Workshop May 23-24, 2018
Roadway Applications Using TDA Joaquin Wright
Senior Project Manager, TDA specialist
+ 46 Associate Members

## Slide 2: ROADWAY APPLICATIONS USING TDA
PRESENTED BY:
Joaquin Wright, GHD Inc.
TO:
NRRA
5/23/18

## Slide 3: Todays Presentation
Introduction to TDA in California Video
Roadway Applications in California

## Slide 4: CalRecycle’ s Objective is to promote the use of TDA in Civil Engineering Applications
Educate Local Public Works, CALTRANS, Private Consulting Civil Engineers and State and Local Environmental Agencies on the benefits of TDA
  Engaged with National Scrap Tire Work Group
Research – Develop Sustainable, Environmental Beneficial and Cost Effective Civil Engineering Reuses for Waste Tires
Coordinate and Assist Waste Tire Processors to assure there is adequate TDA to meet future demand.

## Slide 5: Beneficial Properties of Tire Derived Aggregate (TDA) in Civil Engineering Applications
Tire Derived Aggregate (TDA) has properties that civil engineers, public works directors & contractors need
  Lightweight
  Free Draining/High Permeability
  Low earth pressure
  Good thermal insulation, .2 Cal/m-hr C
    >5x better then soil
    Does not hold moisture or “wick”, therefore no decreased performance due to water
  Durable
  Compressible
  May be cheapest solution
  Helps the environment when used in sustainable infrastructure
  Conserve natural aggregate resources

## Slide 6: TDA ASTM Guidelines D6270 -2017
  Construction practices
    Design and Construction guidelines
      Geotextile separator
      10 ft lifts
      Compacted dry density of ~50lbs/cf
      min. 10 tons vibratory steel wheel compactor, six passes
  Material Specifications
    Type A, 2-4 inch nominal
    Type B, 6-12 inch nominal
  Leachate
    TDA can be placed Above and Below water table with negligible effects on water quality.

## Slide 7: TDA Gradation Specification
Sample Gradation of TDA

## Slide 8: Roadway Uses for Tire Derived Aggregate
Lightweight fill for Road Embankments
Lightweight fill for Road Slide Repair
TDA in Low Impact Development (LID) Roadway Storm-Water infiltration galleries

## Slide 9
Dixon Landing/HWY 880 Interchange Project
Embankment Projects

## Slide 10: 660,000 Tires
DIXON LANDING
TYPE B TDA

## Slide 12
Confusion Hill Embankment Project

## Slide 13
Confusion Hill - Lightweight TDA Embankment Project 2008
270,000 Tires
TYPE B TDA
Notes: This project started in this summer and is being constructed in 4 phases. Placement of all the TDA will be completed next year.
This project will use 270,000 PTE’s of TDA and will save the State of California approximately $320,000.

## Slide 14
Confusion Hill
Final Project

## Slide 15
2007 – Marina Drive, Mendocino Co. Landslide Repair
2008 - Sonoma Co. Geysers Rd. Landslide Repair Project
2009 - Sonoma Mtn. Road , Landslide Repair Project
2012 – Santa Barbara, Palomino Road
Slide Repair Projects

## Slide 16
Marina Drive Slide Repair

## Slide 17
133,000 Tires
Mendocino County, Marina Dr.
TYPE B TDA

## Slide 18
Marina Drive Slide Repair
Savings to the County $90,000

## Slide 19
Geysers Road Slide

## Slide 20
150,000 Tires
Geysers Road Slide Repair
TYPE B TDA
Notes: PROJCT OVERVIEW

## Slide 21
Savings to County $128,000
Geysers Road
Before
After

## Slide 22: Sonoma Mtn. Road, Sonoma County
Notes: The Sonoma Mountain Road in Glen Ellen is also a slide repair project in Sonoma county that is currently under construction.
Sonoma Mountain Road failed back in 2006 and has been completely closed since then.
After agreeing to work with the county on the Geysers Road slide project the County came for the Board with this project. They had hoped it to would be a good candidate for a TDA project. In an effort to get the county to more comfortable with using TDA on their own the CIWMB agreed to supply the TDA material for the project and provide construction oversight for the TDA placement.
The county is responsible for the design and implementation of the construction.

## Slide 23: Sonoma Mountain Road
330,000 TIRES
TYPE B TDA

## Slide 24: Sonoma Mtn. Road, Sonoma County
Savings to County $590,000

## Slide 25: Palomino Road, Santa Barbara County Slide Repair

## Slide 26: Palomino Road, Slide Repair
Savings to County $90,000

## Slide 27
Light Weight Backfill Behind Retaining Walls
TYPE B TDA

## Slide 28
Riverside, CA
Final geo-textile wrap

## Slide 29
Estimated Savings on Future Walls - $200/ lineal foot
Type 1 T Retaining Walls

## Slide 30
Estimated Savings on Future Walls - $200/ lineal foot
Type 1 T Retaining Walls

## Slide 31
Estimated Savings on Future Walls - $200/ lineal foot
Type 1 T Retaining Walls

## Slide 32
TDA In Light Rail Vibration Mitigation

## Slide 33: Conventional Vibration Mitigation Technology $800+/ft

## Slide 34
TDA Vibration Mitigation $150/ft

## Slide 35: TDA LID Designs
Butte Regional Transit Operations Center (BRTOC), Chico, CA
Fleet and Materials Lab Building, Santa Rosa, CA
Transportation Improvements for Redwood Business Park, Ukiah, CA
  In Construction now

## Slide 36: BRTOC Project Site Plan

## Slide 37: Bioretention Swale Typical Section

## Slide 38: BRTOC Construction Photos

## Slide 39: BRTOC Construction Photos

## Slide 40: BRTOC Construction Photos

## Slide 41: BRTOC Construction Photos
Helical Soil Anchor

## Slide 42: BRTOC Construction Photos

## Slide 43: BRTOC Construction Photos

## Slide 44: BRTOC Construction Photos

## Slide 45: BRTOC Construction Photos

## Slide 46: Sonoma County Fleet Facility Site Plan

## Slide 47: Bioretention Swale Typical Section

## Slide 48: Fleet Facility Site Construction Photos

## Slide 49: Fleet Facility Site Construction Photos

## Slide 50: Fleet Facility Site Construction Photos

## Slide 51: Fleet Facility Site Construction Photos

## Slide 52: Fleet Facility Site Construction Photos

## Slide 53: City of Ukiah Redwood Business Park Typical Road Reconstruction & LID Plan

## Slide 54: TDA Infiltration gallery cross section view
BIORETENTION TDA AREA

## Slide 55: Typical Infiltration Gallery (Pre-Construction)
Catch Basin
Bioretention TDA Area
Perf Pipe
Cleanout

## Slide 56: Typical Infiltration Gallery (excavation & fill)

## Slide 57: Typical Infiltration Gallery

## Slide 58: ?

## Slide 59
Thank You