MnDOT District:	X

This template is provided as a starting document for development of a Plan of Action (POA).  The document must be customized for each bridge. Optional comments, template instructions are provided in blue font and should be removed for the final POA product.

In general the POA should be streamlined (1-2 pages long) and focus on providing information that the inspector needs to know when out in the field.  We are assuming the inspector has access to a bridge plan, previous inspection reports (including the inventory sheet), historical cross-section and other data.

The POA consists of several sections, General Information, History and Recommended Action.

POAs should be reviewed periodically and updated as needed.

Route:	TH X	Location:	XX Miles Southeast of XX

Stream:	XXXXX River	County:	XXXX

Scour Code:	P – Stable Due To Protection

Prepared:	preparers name   x/x/2008

Approved:	                                             	     County Engineer

County Bridge Engineer/Supervisor

Sign and date approvals

HISTORY

Provide scour countermeasure information:

- Type of protection, description of countermeasure, date protection installed,

- Reason protection needed, explanation of any scour or other damage that resulted in the need for protection.

Insert additional history if relevant. Consider if any of the following items should be included:

- Source of critical scour code: observed, assessed, calculated, other

- Year built, year rebuilt

- Foundation type

- Number of spans, type of structure

- Scour history, any problems related to scour or erosion.

- Additional consideration or critical issue such as road overtopping, debris potential, etc.

RECOMMENDED ACTION

This bridge structure has been determined to be stable due to protection.  There is a possibility that protection could deteriorate over time or fail during large floods.  The riprap for the bridge should be inspected during routine inspections and after major flood events.  Evaluate the condition and extent of protection to determine if repairs are necessary.  Take cross-sections at the upstream and downstream fascias at intervals not to exceed five years. A record of these cross-sections shall be kept and results compared over time.

If riprap is determined to be missing or critical scour elevation is reached, immediately contact the County Engineer. Develop repair recommendations. The following information is provided when monitoring during or after a flood:

Customize headings

| Structure | Top of Railing Elevation | To p of Footing Elevation or Bottom of Planking Elevation | Bottom of Footing Elevation or Bottom of Piling Elevation | Critical Scour Elevation | Top of Riprap Elevation |
| --- | --- | --- | --- | --- | --- |
| North Abutment | XXX.X | XXX.X | XXX.X | XXX.X | Variable1 |
| Pier 1 | XXX.X | XXX.X | XXX.X | XXX.X | XXX.X |
| South Abutment | XXX.X | XXX.X | XXX.X | XXX.X | Variable1 |

Datum: provide elevation datum

1  Riprap is installed on a slope.  Take a baseline cross-section, use to compare against future measurements.

- Add and delete rows in table as necessary

- Reference may be top of rail or top of curb

-Typical accuracy of elevations to tenth of a foot i.e. 900.2