## Slide 1: Seismic Approach to Quality Management of HMA
Principal Investigator: Choon Park, Park Seismic LLC, Shelton, Connecticut, USA
Co-Investigators: Nils Ryden and Josefin Starkhammar, Norfee Tech, Lund, Sweden
Administrative Staff: Jin Park, Park Seismic LLC, Shelton, Connecticut, USA
Presented By
Choon Park, Ph.D.
Park Seismic LLC

## Slide 2
Hot Mix Asphalt (HMA) Pavement
Stiffness (e.g., Vs) and Thickness (H)
Construction and Maintenance

## Slide 3
  Conventional (Coring, Density, Gravity, etc.)
  Indirect stiffness
  Spot checking
  Destructive
Seismic (Elastic) Wave Approach
  Direct stiffness (“Elasticity”)
  Non-destructive
  Continuous 2D & 3D
HMA  How to Measure Vs and H
Conventional
Seismic

## Slide 4
  Multichannel Analysis of Surface Waves (MASW) (Park et al., 1999)
  Shear-wave velocity (Vs) (1D, 2D, and 3D)
  Vs  Direct indicator of “stiffness” [e.g., Young’s (E) and shear ()]
Seismic Approach  MASW
MASW

## Slide 5
Previous Project at MnDOT  CEMS
(Park and Richter, 2017)
THIS
Project
Previous (CEMS)
  Geophone approach (50 – 1000 Hz) with target depths ≥ 0.5 m
  This (HMA) project  target depths ≤ 0.3 m (1-25 Khz)
Compaction Evaluation by MASW Surveys (CEMS)

## Slide 6
Vs = 1500 m/s
Vs = 1450 m/s
Vs = 1350 m/s
H = 0.15 m
H = 0.12 m
H = 0.10 m
HMA Stiffness (Vs)
HMA Thickness (H)
POS = 0.40
POS = 0.35
POS = 0.30
HMA Poisson’s Ratio (POS)
HMA and Dispersion Curve  How
(H = 0.1 m)
(Vs = 1500 m/s)
(H = 0.1 m, Vs = 1500 m/s)
Accuracy ≥ 98%
Accuracy ≥ 95%

## Slide 7
Pavement MASW (Ryden et al., 2004)
I-70 (Manhattan, KS)
Lamb wave (A0)
Contact measurements with accelerometer and a small hammer.

## Slide 8
Non-Contact Pavement MASW
(Ryden et al., 2006)
Surface wave
Surface wave
Leaky
surface wave

## Slide 9
Shear wave velocity (m/s)
Test line 4.0 m
Non-Contact-Rolling Pavement MASW
(Bjurström and Ryden, 2017)
48 MEMS microphone array (1-cm spacing)
Solenoid impact source

## Slide 10
THIS PROJECT
10 – 30 MPH
On-Board Real Time Display
~6 ft
~2 ft

## Slide 11
PROPOSERS

## Slide 12
Hardware (Dr. Starkhammar & Dr. Ryden)
  Multichannel Acquisition Device (MAD) (e.g., 60 channels)
  MEMS Microphone Arrays (MMA) (e.g., 3-6 linear arrays with 10-channel/array)
  Rolling Impact Source (RIS) (e.g., one or an array of flying steel balls)
  Frame (MAD + MMA) + RIS
Software and General Oversight (Dr. Park)
  Acquisition Control Module (Pseudo AUTO)
  QA/QC Module (Full AUTO)
  On-Board Real-Time Analysis/Display Module (Full AUTO)
  Post-Acquisition Extended Analysis Module (Manul-AUTO)
Administration (Dr. Jin Park)
  Monthly Conference (Skype)
  Managing Dedicated Secure Website
  Travel and Joint Field Test Arrangement
  Financial Management
  Quarterly and Final Report
WORK PLAN & DELIVERABLES

## Slide 13
WORK PLAN AND SCHEDULE
May, 2022

## Slide 14
Category | Amount ($)
Direct Labor Costs: | 134,504.00
Direct Expense Costs: | 12,940.00
Subcontractor Costs: (Norrfee Tech, AB) | 152,442.00
Totals: | 299,886.00
PROJECT BUDGET
DETAILS
SUMMARY

## Slide 15
RECENT DEVELOPMENTS AND PROJECTION
Microphone array
(MEMS*)
(Modified car bicycle rack)
(Rest of hardware
kept in trunk)
*Micro-Electro-Mechanical Sensor

## Slide 16
Microphone array close-up (Top)
Connectors to for cables
leading the analogue signal to
A/D converting hardware
Each of these are
microphones
48 channels → “super stereo recording”
Connectors for batteries supplying the microphones with power

## Slide 17
The 48 microphone acoustic
ducts face the pavement during
recordings
Microphone array close-up (Bottom)
0.75 cm

## Slide 18
48 parallel A/D converters from National Instruments
Data acquisition controlled though LabVIEW-program on regular PC in rack form, from National Instruments
PXI rack holding digitizer cards
(A/D conversion) and controller
(PC in rack format)
PC screen monitor. In field measurements, this monitor is replaced by a rugged laptop with wireless connection to the PXI rack
Entire A/D System

## Slide 19
Rolling-Impact Source  “Bouncing Steel Ball”!
Bouncing ball source!

## Slide 20
Rolling-Impact Source  “Bouncing Steel Ball”!